## Slide 1
Electron Cloud Effects: Heat Load and Stability Issues
G. Iadarola, A. Axford, K. Li, A. Romano, G. Rumolo
Joint HiLumi LHC - LARP Annual Meeting, 11-13 November 2015, Fermilab, USA
Acknowledgments:
H.Bartosik, R. De Maria, C. Garion, A. Oeftiger, M. Schenk, R. Tomas

## Slide 2
e-cloud in the LHC: where do we stand
  Run 1 experience has shown that electron cloud effects can limit the achievable performance with 25 ns beams mainly through beam degradation at low energy and high heat load at high energy
    Two scrubbing runs scheduled for 2015 (>20 days in total starting in June) to lower SEY of the beam chamber and allow 25 ns physics
    Special scrubbing beam (“doublet”) in preparation in the injectors
    Important experience in order to quantify how effectively scrubbing can mitigate e-cloud effects  important input for HL-LHC

## Slide 3
Buildup simulations for the HL-LHC
  Impact of HL-LHC beam parameters estimated by PyECLOUD simulation for several machine components (mainly cold magnets)
  Multipacting threshold and heat load estimated for:
    Arc main magnets
    Matching quadrupoles (present and HL-LHC design)
    Separation/recombination dipoles(present and HL-LHC design)
    Inner triplets (present and HL-LHC design)
  Ongoing development to study the impact of shields at the pumping holes (baffles)
Details can be found in:
G. Iadarola et al., “Beam induced heat load in the cold elements of the IRs”, at LARP-HiLumi Meeting, 20 November 2015, KEK – Japan
G. Rumolo et al., “Progress on electron cloud studies for HL-LHC”, at 48th HiLumi WP2 Task Leader Meeting, 24 April 2015, CERN

## Slide 4
e-cloud in the arc main magnets
  For cold magnets in the arcs we will have to rely on beam induced scrubbing also in the HL-LHC era
Nominal
HL-LHC
    Stronger heat load in the HL-LHC mainly for large values of SEY
    Scrubbing should allow us to achieve SEY<1.3  e-cloud suppression in the dipoles
      Heat load in the arcs within cryo cooling capacity
      But e-cloud still present in the quadrupoles
  What is the effect on beam stability/degradation?

## Slide 5
The PyECLOUD-PyHEADTAIL simulation setup
  Impact of e-cloud on beam quality/stability is usually estimated by MacroParticle (MP) simulations
  Unfortunately the available tool (HEADTAIL) could not handle the required simulation scenarios (quadrupole field, non negligible impact of the beam chamber)
   Important code development activity the last year in the framework of a much broader reorganization of our simulation tools:
Monolithic code
HEADTAIL
Modular and scriptable tool
PyHEADTAIL
See also: K. Li, “PyHEADTAIL”, at BE-ABP information meeting, 12 March 2015, CERN

## Slide 6
PyHEADTAIL
v
The PyECLOUD-PyHEADTAIL simulation setup
  We dropped the traditional approach of having separate tools for ecloud buildup and instability
  Use PyECLOUD also simulate the interaction beam/ecloud within PyHEADTAIL
     Possible thanks to the highly modular structure of the two codes (object oriented)
PyHEADTAIL bunch
PyHEADTAIL slicer
For each slice
PyHEADTAIL bunch
PyECLOUD
(PyEC4PyHT object)
Evaluate beam slice electric field (Particle in Cell)
Generate seed e-
Compute e- motion (t->t+Δt)
(possibly with substeps)
Detect impacts and generate secondaries
Evaluate the e- electric field
(Particle in Cell)
Apply kick on the beam particles
Legend: From PyHEADTAIL From PyECLOUD Developed ad hoc
Initial e- distribution
(from PyECLOUD buildup sim.)
PyHEADTAIL
Transverse tracking
   with Q’, octupoles etc.
Longitudinal tracking
Transverse feedback
Impedances
Space charge
…
Transverse tracking
   with Q’, octupoles etc.
Longitudinal tracking
Transverse feedback
Impedances
Space charge
…

## Slide 7
The PyECLOUD-PyHEADTAIL simulation setup
  We dropped the traditional approach of having separate tools for ecloud buildup and instability
  Use PyECLOUD also simulate the interaction beam/ecloud within PyHEADTAIL
     Possible thanks to the highly modular structure of the two codes (object oriented)
  Advantages of this approach:
    Profits from years of optimization and testing work on PyECLOUD and PyHEADTAIL
    All advanced e-cloud modeling features implemented in PyECLOUD become naturally available for beam dynamics simulations
    From now on the two tools can share most of the work of development and maintenance
  Extensive tests against HEADTAIL in the last year:
    Single e-cloud interaction
    Single turn
    Tune footprint
    E-cloud instabilities
  Since ~2 months the new code is being used for instabilities simulation campaigns for LIU-SPS and HL-LHC studies (though with simplified model at this stage, i.e. uniform beta function, uniform initial e- distribution)

## Slide 8
e-cloud instability simulations for the HL-LHC
We simulated the interaction of a single bunch with the electron cloud in the dipoles and in the quadrupoles separately scanning the bunch intensity and the electron density
Before the bunch passage electrons are uniformly distributed and at rest in the chamber
Parameter | Value @ 450 GeV | Value @ 7 TeV
N (p/b) | 1.3 – 2.3 x 1011 | 1.3 – 2.3 x 1011
ex,y (mm) | 2.5 | 2.5
sz (m) | 0.1 | 0. 075
B (T, T/m) | 0.53, 12 | 8.2, 187
V400MHz (MV) | 8 | 16
Nel (e-/m3) | 0.3 – 20 x 1012 | 0.3 – 20 x 1013
Nsegments | 79 | 31
NMP (e-) | 105 | 105
NMP (p) | 3 x 105 | 3 x 105
Nslices (-2sz, 2sz) | 64 | 64
Qx, Qy | 62.28 | 60.31
<βx>, <βy> | 92.7 | 93.2

## Slide 9
e-cloud instability thresholds: Arc Dipoles
Instability observed only in the vertical plane, as the dipole magnetic field freezes the electron motion in the horizontal plane (note that, unlike HEADTAIL, electrons are tracked also in the horizontal plane)
Arc dipoles (~65% of the machine)
N = 2.3 x 1011 p/b

## Slide 10
N = 2.3 x 1011 p/b
e-cloud instability thresholds: Arc Dipoles
Instability observed only in the vertical plane, as the dipole magnetic field freezes the electron motion in the horizontal plane (note that, unlike HEADTAIL, electrons are tracked also in the horizontal plane)
Dependence of the instability threshold on bunch intensity is quite weak:
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 1.2 x 10 12 e-/m3 | 1 x 10 12 e-/m3 | 1 x 10 12 e-/m3
Arc dipoles (~65% of the machine)

## Slide 11
e-cloud instability thresholds: Arc Dipoles
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 1.2 x 10 12 e-/m3 | 1 x 10 12 e-/m3 | 1 x 10 12 e-/m3
Arc dipoles (~65% of the machine)
PyECLOUD buildup simulations – 2.3e11 ppb
Comparing against buildup simulation results:
SEY > 1.5 needed for the ecloud in the dipoles alone to drive an instability

## Slide 12
e-cloud instability thresholds: Arc Quadrupoles
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 9 x 10 12 e-/m3 | 9 x 10 12 e-/m3 | 10 x 10 12 e-/m3
Arc qudrupoles (~5% of the machine)
N = 2.3 x 1011 p/b
Dependence on bunch intensity is quite weak
Instability observed in both planes, consistently with the symmetry of the e-cloud dynamics in the quadrupoles

## Slide 13
e-cloud instability thresholds: Arc Quadrupoles
Dependence on bunch intensity is quite weak
Instability observed in both planes, consistently with the symmetry of the e-cloud dynamics in the quadrupoles
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 9 x 10 12 e-/m3 | 9 x 10 12 e-/m3 | 10 x 10 12 e-/m3
Arc qudrupoles (~5% of the machine)
N = 2.3 x 1011 p/b

## Slide 14
e-cloud instability thresholds: Arc Quadrupoles
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 9 x 10 12 e-/m3 | 9 x 10 12 e-/m3 | 10 x 10 12 e-/m3
Arc qudrupoles(~5% of the machine)
PyECLOUD buildup simulations – 2.3e11 ppb
Comparing against buildup simulation results:
For reasonable values of the SEY (i.e. after scrubbing) e-cloud in the quadrupoles alone too weak to drive an instability

## Slide 15
Instability thresholds at high energy: a first look
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 1.2 x 10 12 e-/m3 | 1 x 10 12 e-/m3 | 1 x 10 12 e-/m3
7 TeV | 8 x 10 12 e-/m3 | 8 x 10 12 e-/m3 | 9 x 10 12 e-/m3
Arc dipoles (~65% of the machine)
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 9 x 10 12 e-/m3 | 9 x 10 12 e-/m3 | 10 x 10 12 e-/m3
7 TeV | 1.2 x 10 14 e-/m3 | 1.1 x 10 14 e-/m3 | 1.2 x 10 14 e-/m3
Arc quadrupoles (~5% of the machine)
Preliminary!!
Preliminary!!
The threshold e- density for transverse instability increases by one order of magnitude going to 7 TeV  effect of increased beam rigidity
Simulations at 7 TeV are numerically more challenging due to the smaller beam size (need for finer grid) and stronger magnetic fields (need fro smaller time steps to resolve electron motion)

## Slide 16
Instability thresholds at high energy: a first look
 | 1.3 x 10 11 ppb | 1.8 x 10 11 ppb | 2.3 x 10 11 ppb
450 GeV | 9 x 10 12 e-/m3 | 9 x 10 12 e-/m3 | 10 x 10 12 e-/m3
7 TeV | 1.2 x 10 14 e-/m3 | 1.1 x 10 14 e-/m3 | 1.2 x 10 14 e-/m3
Arc quadrupoles (~5% of the machine)
Preliminary!!
The threshold e- density for transverse instability increases by one order of magnitude going to 7 TeV  effect of increased beam rigidity
PyECLOUD buildup simulations
Quadrupoles: increase in energy has an important impact also on the e-cloud buildup due to the gradient increase
 Densities still well below instability threshold for reasonable values of SEY

## Slide 17
Tune footprint due to e-cloud in the Arc Dipoles
Even below the instability threshold e-cloud is exerting forces on beam particles
   Tune footprint
Electrons are free to move only in the vertical plane: footprint is asymmetric
Instantaneous footprint obtained with frozen longitudinal motion and “recorded” e- pinch

## Slide 18
Tune footprint due to e-cloud in the Arc Dipoles
Even below the instability threshold e-cloud is exerting forces on beam particles
   Tune footprint
Electrons are free to move only in the vertical plane: footprint is asymmetric

## Slide 19
Tune footprint due to e-cloud in the Arc Dipoles
Vertical plane: tune spread dominated by e-cloud density inside the bunch  Positive tune shift
e- pinch and density oscillations clearly visible on tunes along the bunch
z [m]

## Slide 20
Tune footprint due to e-cloud in the Arc Dipoles
Horizontal plane: tune spread smaller than in vertical
Defocusing effect at bunch tail due to large density on bunch side

## Slide 21
Tune footprint due to e-cloud in the Arc Quadrupoles
Even below the instability threshold e-cloud is exerting forces on beam particles
   Tune footprint
Symmetry of the B field map translates into a symmetric footprint

## Slide 22
Tune footprint due to e-cloud in the Arc Quadrupoles
Even below the instability threshold e-cloud is exerting forces on beam particles
   Tune footprint
Symmetry of the B field map translates into a symmetric footprint

## Slide 23
Tune footprint due to e-cloud in the Arc Quadrupoles
Even below the instability threshold e-cloud is exerting forces on beam particles
   Tune footprint
Symmetry of the B field map translates into a symmetric footprint

## Slide 24
Arc Quadrupoles: realistic e- distribution
Tune footprint
(uniform initial distribution)
Tune footprint
(initial distribution from buildup sim.)
Simulations for nominal bunch intensity
First test performed with self consistent distribution from buildup simulation
  Significant impact on the footprint!

## Slide 25
Arc Quadrupoles: realistic e- distribution
z [m]
y [m]
z [m]
y [m]
First test performed with self consistent distribution from buildup simulation
  Significant impact on the footprint!
  Electrons trapped along the magnetic  pinch is attenuated
Uniform initial distribution
Initial distribution from buildup simulation

## Slide 26
Summary and conclusions
  For the main magnets in arcs we will have to rely on beam induced scrubbing to mitigate e-cloud effects also in the HL-LHC era
    Full suppression should be possible for the arc dipoles but seems unlikely for the quadrupoles
    Heat loads should be within the cryo cooling capacity but impact on beam quality/stability needs to be assessed
    Important development work (PyECLOUD-PyHEADTAIL simulation setup) carried out in the latest year to allow the simulation of this kind of scenario  test & validation of the new tool done
    First simulation campaign for HL-LHC arc main magnets:
    After SEY reduction through beam induced scrubbing (SEY < 1.3) e-cloud should not drive the beam unstable…
    … but still important forces on the beam  tune spread
    First simulations at high energy show that at 7 TeV instability threshold density is 10 times larger than at 450 GeV (increased beam rigidity)
  First tests performed with e-cloud distribution from buildup simulation show significant change with respect to the corresponding cases with uniform initial distribution (especially for the quadrupoles)
   Instability threshold and footprint to be updated with self-consistent distributions

## Slide 27
Thanks for your attention!

## Slide 28
Parameter | Value @450 GeV | Value @7 TeV
N (p/b) | 1.3 – 2.3 x 1011 | 1.3 – 2.3 x 1011
ex,y (mm) | 2.5 | 2.5
sz (m) | 0.1 | 0. 075
B (T, T/m) | 0.53, 12 | 8.2, 187
V400MHz | 8 MV | 16 MV
Nel (e-/m3) | 0.3 – 20 x 1012 | 0.3 – 20 x 1012
Nsegments | 79 | 31
NMP (e-) | 105 | 105
NMP (p) | 3 x 105 | 3 x 105
Nslices (-2sz, 2sz) | 64 | 64
Qx, Qy | 62.28 | 60.31
<βx>, <βy> | 92.7 | 93.2
Sync period | ~200 turns | ~500 turns

## Slide 30
From buildup
Uniform