## Slide 1
Electron cloud studies for CERN particle accelerators and simulation code development
Doctoral thesis by: Giovanni Iadarola
Tutors: Giovanni Miano, Giovanni Rumolo
Napoli, 23 May 2014
Università degli Studi di Napoli Federico II
European Organization for Nuclear Research (CERN)

## Slide 2
Outline
  Introduction
    The Large Hadron Collider (LHC)
    Electron Cloud effects
  PyECLOUD: a new code for e-cloud buildup simulation
    MacroParticle size management
    Performances
  E-cloud experimental studies at the LHC
    Motivation
    e-cloud effects with 25 ns beams at the LHC
    Studies for a dedicated scrubbing beam

## Slide 3
Outline
  Introduction
    The Large Hadron Collider (LHC)
    Electron Cloud effects
  PyECLOUD: a new code for e-cloud buildup simulation
    MacroParticle size management
    Performances
  E-cloud experimental studies at the LHC
    Motivation
    e-cloud effects with 25 ns beams at the LHC
    Studies for a dedicated scrubbing beam

## Slide 4
The Large Hadron Collider (LHC)
  Largest and most powerful particle accelerator ever built (27 km circumference)
  It is designed to:
  store 450 GeV protons (in two counter rotating beams)
  accelerate them up to 7 TeV
  collide the two beams in four points of the ring (for high energy physics experiments)
Beam 1
Beam 2

## Slide 5
The Large Hadron Collider (LHC)
  Largest and most powerful particle accelerator ever built (27 km circumference)
  It is designed to:
  store 450 GeV protons (in two counter rotating beams)
  accelerate them up to 7 TeV
  collide the two beams in four points of the ring (for high energy physics experiments)
Beam 1
Beam 2

## Slide 6
The Large Hadron Collider (LHC)
  Largest and most powerful particle accelerator ever built (27 km circumference)
  It is designed to:
  store 450 GeV protons (in two counter rotating beams)
  accelerate them up to 7 TeV
  collide the two beams in four points of the ring (for high energy physics experiments)
Beam 1
Beam 2
Injection
(~ 30 min.)
Acceleration
(~20 min.)
Prepare
for collision
(~30 min.)
Collisions
(several hours)
A typical LHC fill

## Slide 7
The Large Hadron Collider (LHC)
  8-fold symmetric structure:
  8 Long Straight Sections (LSS) to host experiments and other equipment
  8 Arcs (2.45 km each - Periodic magnet lattice to bend and focus the beams)
  8.33 T dipoles
  223 T/m quadrupoles
  Main magnets
  (superconducting)

## Slide 8
The Large Hadron Collider (LHC)
  8-fold symmetric structure:
  8 Long Straight Sections (LSS) to host experiments and other equipment
  8 Arcs (2.45 km each - Periodic magnet lattice to bend and focus the beams)
  8.33 T dipoles
  223 T/m quadrupoles
  Main magnets
  (superconducting)
    Superconducting coils (1.9 K)
    Beam screen (5 – 20 K)
    Beam screen cooling circuit
    (liquid helium)
  Section of a main dipole

## Slide 9
Outline
  Introduction
    The Large Hadron Collider (LHC)
    Electron Cloud effects
  PyECLOUD: a new code for e-cloud buildup simulation
    MacroParticle size management
    Performances
  E-cloud experimental studies at the LHC
    Motivation
    e-cloud effects with 25 ns beams at the LHC
    Studies for a dedicated scrubbing beam

## Slide 10
The electron cloud buildup
    Proton bunch
    e- is emitted (photoelectric effect)

## Slide 11
The electron cloud buildup
    Proton bunch
    e- is emitted (photoelectric effect)
Secondary Electron Emission
SEY:

## Slide 12
The electron cloud buildup
    If the SEY is large enough, Secondary Electron Emission can drive an avalanche multiplication effect filling the beam chamber with an electron cloud
    Proton bunch
    e- is emitted (photoelectric effect)

## Slide 13
The electron cloud buildup
    The electron density grows exponentially during the passage of the bunch train and then saturates (due to space charge effects within the cloud)
    The trailing bunches of the train see the largest electron density

## Slide 14
The electron cloud buildup
    The electron density grows exponentially during the passage of the bunch train and then saturates (due to space charge effects within the cloud)
    The trailing bunches of the train see the largest electron density
Something like this…

## Slide 15
The electron cloud buildup
    The presence of electron clouds in the beam chamber can have serious impact on the machine performance. The most common effects are:
    Transverse beam instabilities (e.g. exponentially growing oscillation of beam position)
    Transverse beam blow-up
    Particle losses
    Vacuum degradation
    Heat load (critical in cryogenic magnets)
LHC Beam 1, 25 ns bunch spacing
Transverse emittance [a.u.]

## Slide 16
Outline
  Introduction
    The Large Hadron Collider (LHC)
    Electron Cloud effects
  PyECLOUD: a new code for e-cloud buildup simulation
    MacroParticle size management
    Performances
  E-cloud experimental studies at the LHC
    Motivation
    e-cloud effects with 25 ns beams at the LHC
    Studies for a dedicated scrubbing beam

## Slide 17
Ingredients for e-cloud build-up simulation
  1. Seed electrons generation
  (gas ionization, photoemission)
  2. Force exerted by the beam on e-
  3. Force exerted by the e- on each other
  (space charge)
  4. Equations of motion
  (also in presence of an external magnetic field)
  5. Secondary emission

## Slide 18
PyECLOUD
  Several key features completely redesigned:
  Beam field computation
    Finite Difference  arbitrary chamber shape
    Pre-saved map & interpolation  improved accuracy and speed
  Electron cloud space charge
  Particle In Cell  arbitrary chamber shape,
  improved accuracy and speed
  Electron tracking
    Semi analytic algorithm for strong non uniform B field time step larger than cyclotron period  simulations for quadrupole and combined function magnets
    Boris tracker  long term accuracy
  Macroparticle Size Management
    See next slides…
  Written in Python (object oriented, open source)
    Easy to develop and test (fundamental! we run thousands of simulations, a bug can waste months of work)
    Flexible to extend (analysis of experimental data from CERN accelerators requires to simulate non ideal, complex situations… see second part of the talk)
  PyECLOUD is the EC buildup code developed during my PhD activity
  In depth analysis of previously available tools  Small improvements practically everywhere

## Slide 19
Macroparticle size management
  To make the computation affordable, the electrons are grouped in MacroParticles (MPs)
  In an electron-cloud buildup, due to the multipacting process, the electron number extends over several orders of magnitude
  It is practically impossible to choose a MP size that is suitable for the entire simulation (allowing a satisfactory description of the phenomenon and a computationally affordable number of MPs)
72 bunches – 25ns spac.
72 bunches – 25ns spac.

## Slide 20
Macroparticle size management
x
  A reference MP size Nref (dynamically adapted during the simulation) is used to “take decisions”:
  Seed MP generation: the generated MPs have size Nref
  Secondary MP emission: additional true secondary MPs are emitted if the total emitted charge is >1.5Nref
  MP cleaning: at each bunch passage a clean function is called to eliminate all the MPs with charge <10-4Nref
72 bunches – 25ns spac.
72 bunches – 25ns spac.

## Slide 21
Macroparticle size management
10.
MP
ref. size [m-1]
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 22
Macroparticle size management
10.
MP
ref. size [m-1]
MP reg.
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 23
  The reference MP size Nref is adaptively changed during the simulation:
Macroparticle size management
10.
MP
ref. size [m-1]
MP reg.
MP set regeneration
  Each macroparticle is assigned to a cell of a uniform grid in the 5-D space (x,y,vx,vy,vz) obtaining an approximation of the phase space distribution
  The new target MP size is chosen such that:
  A new MPs set, having the new reference size, is generated according to the computed distribution
  The error on total charge and total energy does not go beyond 1-2%

## Slide 24
Macroparticle size management
10.
45.
MP
ref. size [m-1]
MP reg.
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 25
Macroparticle size management
10.
45.
MP
ref. size [m-1]
MP reg.
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 26
Macroparticle size management
10.
45.
MP
ref. size [m-1]
MP reg.
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 27
Macroparticle size management
10.
45.
2.1e2
1.1e3
5.5e3
2.9e4
1.3e5
3.1e5
3.6e5
MP
ref. size [m-1]
MP reg.
  The reference MP size Nref is adaptively changed during the simulation:

## Slide 28
Impact on the simulation performances
ECLOUD (old code)
PyECLOUD
  SPS MBB bending magnet, SEYmax = 1.5, nominal 25 ns beam, E=26 GeV
  The newly introduced features had an evident impact on convergence properties and speed

## Slide 29
Impact on the simulation performances
  SPS MBB bending magnet, SEYmax = 1.5, nominal 25 ns beam, E=26 GeV
Timestep | ECLOUD | PYECLOUD
0.2 ns | 29 min | 12 min
0.1 ns | 1h 27 min | 13 min
0.05 ns | 1h 45 min | 24 min
0.025ns | 3h 7 min | 40 min
0.012ns | 4h 15 min | 1h 6 min
Time step
Simulation time [s]
  The newly introduced features had an evident impact on convergence properties and speed

## Slide 30
Impact on the simulation performances
  PyECLOUD has quickly became the reference tool for electron cloud simulations for CERN machines, covering a variety of devices and beam conditions:
  CERN Proton Synchrotron (PS, 26 GeV, 628 m ring)
    Drift chambers, combined function magnets, electron cloud detectors
    Several beam configuration and surface properties
  Super Proton Synchrotron (SPS, 450 GeV, 7 Km ring)
    Drift chambers, dipole magnets, electrostatic septa
    Several beam configuration and surface properties
  Large Hadron Collider (LHC, 7 TeV, 27 Km ring)
    Drift chambers, dipole and quadrupole magnets, injection kickers, beam profile monitor, special common chambers, final focusing triplets
    Several beam configuration and surface properties
  Moreover:
    Positron machines (PETRA III, Hamburg, Germany; CLIC linear collider damping ring – designs study)
    Used in other institutes (FERMILAB, Chicago, USA; LAL, Orsay, France; DESY, Hamburg, Germany, UNISANNIO, Benevento, Italy)
  The newly introduced features had an evident impact on convergence properties and speed

## Slide 31
Outline
  Introduction
    The Large Hadron Collider (LHC)
    Electron Cloud effects
  PyECLOUD: a new code for e-cloud buildup simulation
    MacroParticle size management
    Performances
  E-cloud experimental studies at the LHC
    Motivation
    e-cloud effects with 25 ns beams at the LHC
    Studies for a dedicated scrubbing beam

## Slide 32
  Main goals and activities:
  Analyze of electron cloud related observations during LHC (& injectors) operation
  Propose  organize  perform  analyze dedicated electron cloud experiments aiming at:
    Qualifying the behavior and performance limitations of the accelerators w.r.t. the electron cloud
    Crosscheck and improve our models and simulation codes (to be able to make reliable predictions for future operation scenarios)
    Study possible countermeasures
Experimental activity

## Slide 33
PyECLOUD simulations
  Bunch spacing is a key parameter for electron cloud effects
   it changes the SEY requirement to suppress the electron cloud
Bunch spacing
Bunch spacing
  Bunch spacing:
  25 ns  7.5 m 50 ns  15 m

## Slide 34
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
  We had three years of LHC beam operation: 2010-2012

## Slide 35
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
  We had three years of LHC beam operation: 2010-2012

## Slide 36
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 37
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 38
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation |  |  |  | 
  We had three years of LHC beam operation: 2010-2012
PyECLOUD simulations
  Scrubbing of Cu measured with e- at 500eV (CERN TE-VSC)
Beam induced scrubbing
    Keeping a significant e- flux on the chamber’s walls causes a decrease of the SEY (and hence the e-cloud)  the electron cloud cures itself
    During dedicated Scrubbing Runs we try to provoke as much e-cloud as possible to condition the chamber’s walls

## Slide 39
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 40
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 41
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
  We had three years of LHC beam operation: 2010-2012

## Slide 42
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
  We had three years of LHC beam operation: 2010-2012

## Slide 43
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
Quick historical recap
  We had three years of LHC beam operation: 2010-2012

## Slide 44
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
  We had three years of LHC beam operation: 2010-2012

## Slide 45
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
2013 - 14 | Long shutdown: maintenance and consolidation |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 46
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
2013 - 14 | Long shutdown: maintenance and consolidation |  |  |  | 
2015 - … | 6.5 TeV | 1.15x1011 p+ | 25 ns | 2604 | ~50 fb-1
  We had three years of LHC beam operation: 2010-2012

## Slide 47
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
2013 - 14 | Long shutdown: maintenance and consolidation |  |  |  | 
2015 - … | 6.5 TeV | 1.15x1011 p+ | 25 ns | 2604 | ~50 fb-1
 | Need to stick to nominal bunch population  25 ns mandatory to reach the luminosity goal |  |  |  | 
  We had three years of LHC beam operation: 2010-2012

## Slide 48
Quick historical recap
 | Energy | Bunch population | Bunch spacing | Number of bunches | Integrated Luminosity/ year
Design | 7 TeV | 1.15x1011 p+ | 25 ns | 2808 | 
2010 | 3.5 TeV | 1.2x1011 p+ | 150 ns | 368 | 0.04 fb-1
 | Attempt to switch to 50 ns spacing: failed due to electron cloud effects! |  |  |  | 
2011 | Operation re-started with 75 ns bunch spacing Scrubbing run to lower the SEY and enable 50 ns operation  successful! |  |  |  | 
 | 3.5 TeV | 1.45x1011 p+ | 50 ns | 1380 | 6.1 fb-1
2012 | Thanks to scrubbing from 2011, operation could be resumed with 50 ns spacing |  |  |  | 
 | 4 TeV | 1.7x1011 p+ | 50 ns | 1380 | 23.1 fb-1
2013 - 14 | Long shutdown: maintenance and consolidation |  |  |  | 
2015 - … | 6.5 TeV | 1.15x1011 p+ | 25 ns | 2604 | ~50 fb-1
 | Need to stick to nominal bunch population  25 ns mandatory to reach the luminosity goal |  |  |  | 
  We had three years of LHC beam operation: 2010-2012
  e-cloud effects with 25 ns spacing are much more severe
  Operation with nominal number of bunches experimentally not proved yet
  We needed to:
  Qualify the performance limitations (heat loads, vacuum, beam dynamics)
  Define a possible mitigation strategy
  Addressed in this thesis work both with simulation and experimental studies (mainly in dedicated machine sessions)

## Slide 49
up to ±5mm
~ bunch 25 is the first unstable
  First injection tests with a train of 48b. on 26/08/2011:
  Beam unstable right after injection (dump due to losses after 3 sec)
  Probably driven by e-cloud in the dipoles (mainly vertical motion, trailing bunches of the train)
Electron cloud effects with 25ns: 2011 experience
H. Bartosik, W. Höfle, G. Iadarola, Y. Papaphilippou, and G. Rumolo, “Benchmarking HEADTAIL with electron cloud instabilities observed in the LHC,” Proceedings of ECLOUD12: Joint INFN-CERN-EuCARD-AccNet Workshop on Electron-Cloud Effects, La Biodola, Isola d’Elba, Italy, 2012

## Slide 50
up to ±5mm
~ bunch 25 is the first unstable
  First injection tests with a train of 48b. on 26/08/2011:
  Beam unstable right after injection (dump due to losses)
  Probably driven by e-cloud in the dipoles (mainly vertical motion, trailing bunches of the train)
  The instability could be successfully reproduced using PyECLOUD-HEADTAIL simulations
bunch 26 is the first unstable
Electron cloud effects with 25ns: 2011 experience
H. Bartosik, W. Höfle, G. Iadarola, Y. Papaphilippou, and G. Rumolo, “Benchmarking HEADTAIL with electron cloud instabilities observed in the LHC,” Proceedings of ECLOUD12: Joint INFN-CERN-EuCARD-AccNet Workshop on Electron-Cloud Effects, La Biodola, Isola d’Elba, Italy, 2012

## Slide 51
  First scrubbing tests with 25ns (450 GeV):
  Running with high chromaticity to avoid EC driven instabilities
  Injected up to 2100b. for B1 and 1020b. for B2
  Strong heat load observed in the cryogenic arcs
  Important beam degradation
2011 experience with 25 ns beams: scrubbing tests
Beam 1
Beam 2
Energy
29/06
07/10
24-25/10
14/10

## Slide 52
Electron cloud effects with 25ns: 2011 experience
  We devised a method to reconstruct the SEY of the vacuum chamber based on the heat load measurements from the cryogenics:
  Based on PyECLOUD simulations with measured beam profiles (mandatory to get reliable results)
29/06
07/10
24-25/10
14/10
50ns
25ns threshold @450 GeV
G. Iadarola and G. Rumolo, “Electron cloud in the CERN accelerators (PS, SPS, LHC),” Proceedings of ECLOUD12: Joint INFN-CERN-EuCARD-AccNet Workshop on Electron-Cloud Effects, La Biodola, Isola d’Elba, Italy, 2012.

## Slide 53
Electron cloud effects with 25ns: 2011 experience
  We devised a method to reconstruct the SEY of the vacuum chamber based on the heat load measurements from the cryogenics:
  Based on PyECLOUD simulations with measured beam profiles (mandatory to get reliable results)
29/06
07/10
24-25/10
14/10
50ns
25ns threshold @450 GeV
J. F. Esteban-Müller, P. Baudrenghien, G. Iadarola, T. Mastoridis, G. Papotti, G. Rumolo, E. Shaposhnikova, and D. Valuch, “Synchronous Phase Shift at LHC,” Proceedings of ECLOUD12,La Biodola, Isola d’Elba, Italy, 2012.
  An important benchmark for our models came from bunch by bunch energy loss estimation based on stable phase measurements

## Slide 54
Scrubbing run (450GeV)
(6 – 10 Dec 2012)
MDs with 25ns at 4TeV
(12 – 15 Dec 2012)
Pilot physics run
with 25ns beams
(15 – 17 Dec 2012)
The “25 ns run” in 2012
  More time for experiments with 25 ns beams and large number of bunches
   concentrated the last 10 days of the run
Access + setup for β*=1m
Test fills
at 450 GeV

## Slide 55
Beam 1
Beam 2
The 2012 scrubbing run
  3.5 days of scrubbing with 25ns beams at 450 GeV (6 - 9 Dec. 2012):
  Filling the ring with up to 2748b. (record!) per beam (up to 2.7x1014 p – record!)
  Slow improvement visible on beam quality and heat load in the arcs

## Slide 56
The 2012 scrubbing run
Beam 1
Beam 2
  3.5 days of scrubbing with 25ns beams at 450 GeV (6 - 9 Dec. 2012):
  Filling the ring with up to 2748b. (record!) per beam (up to 2.7x1014 p – record!)
  Slow improvement visible on beam quality and heat load in the arcs

## Slide 57
Experience with 25 ns beams at 4 TeV
Machine Studies
with 25 ns beams at 4TeV
(12 – 15 Dec 2012)
Pilot physics run
with 25ns beams
(15 – 17 Dec 2012)
84b.
156b.
372b.
804b.
804b.
108b.
204b.
396b.
780b.
  The accumulated scrubbing made possible to have machine studies and a pilot physics run with 25 ns at 4 TeV

## Slide 58
<S56>
<S67>
Experience with 25 ns beams at 4 TeV
  A strong enhancement on the heat load is observed on the energy ramp
  Rescaling to the nominal number of bunches it exceeds the cooling capacity of the cryogenics!

## Slide 59
Experience with 25 ns beams at 4 TeV
  A strong enhancement on the heat load is observed on the energy ramp
  Large electron cloud density in the arcs does not show a strong effect on the beam (due to increased beam rigidity)
  Emittance blow-up in collision very similar to 50 ns  likely not due to EC
50 ns
1.45 – 1.6 x 1011 ppb
25 ns
1.0 – 1.1 x 1011 ppb

## Slide 60
Scrubbing: we need to do better!
  Experience in Run 1 showed that the electron cloud can limit the achievable performance with 25 ns beams mainly through:
    beam degradation (blow-up, losses) at low energy
    high heat load on arc beam screens at high energy
    To operate with 25 ns beams (~2800b.) it is mandatory to achieve lower values in SEY
    Dedicated scrubbing beams with hybrid bunch spacing are presently under study
PyECLOUD simulations
LHC dipole
Electron density [a. u.]
Scrubbing beam (5+20) ns
Standard beam 25 ns

## Slide 61
  Experience in Run 1 showed that the electron cloud can limit the achievable performance with 25 ns beams mainly through:
    beam degradation (blow-up, losses) at low energy
    high heat load on arc beam screens at high energy
    To operate with 25 ns beams (~2800b.) it is mandatory to achieve lower values in SEY
    Dedicated scrubbing beams with hybrid bunch spacing are presently under study  production scheme with non adiabatic splitting @ SPS injection
Scrubbing: we need to do better!
25 ns
25 ns

## Slide 62
  Experience in Run 1 showed that the electron cloud can limit the achievable performance with 25 ns beams mainly through:
    beam degradation (blow-up, losses) at low energy
    high heat load on arc beam screens at high energy
    To operate with 25 ns beams (~2800b.) it is mandatory to achieve lower values in SEY
    Dedicated scrubbing beams with hybrid bunch spacing are presently under study  production scheme with non adiabatic splitting
Scrubbing: we need to do better!
25 ns
25 ns

## Slide 63
  Experience in Run 1 showed that the electron cloud can limit the achievable performance with 25 ns beams mainly through:
    beam degradation (blow-up, losses) at low energy
    high heat load on arc beam screens at high energy
    To operate with 25 ns beams (~2800b.) it is mandatory to achieve lower values in SEY
    Dedicated scrubbing beams with hybrid bunch spacing are presently under study  proved experimentally at SPS
Scrubbing: we need to do better!
4
2
6
6
0
1
2
3
Time [ms]
200 MHz RF Voltage [MV]
4
-1
0
1st inj.

## Slide 64
  Experience in Run 1 showed that the electron cloud can limit the achievable performance with 25 ns beams mainly through:
    beam degradation (blow-up, losses) at low energy
    high heat load on arc beam screens at high energy
    To operate with 25 ns beams (~2800b.) it is mandatory to achieve lower values in SEY
    Dedicated scrubbing beams with hybrid bunch spacing are presently under study  proved experimentally at SPS
Scrubbing: we need to do better!
PyECLOUD simulation
Measurement

## Slide 65
  The Electron Cloud Buildup in the LHC and its injector complex has been addressed with simulation and experimental studies
  PyECLOUD, a new code for the simulation of the electron cloud buildup, has been developed
    The newly implemented solutions had a evident impact on accuracy, speed, and usage flexibility (compared to other tools)
  Simulation and experimental studies have addressed the electron cloud issues at the LHC (with particular emphasis on 25 ns bunch spacing)
    Main limitations have been identified (beam degradation at 450 GeV and heat load at 4 – 7 TeV)
    A mitigation strategy (including the use of a specifically designed scrubbing beam) has been defined
Summary

## Slide 66
  Extensive simulation studies for the LHC arc components
    Relative contribution of dipoles and quadrupoles (confirmed experimentally)
    Dependence on bunch intensity, bunch length, transverse size
  Simulation and experimental studies for the LHC interaction regions
    800 mm common chamber at the ALICE experiment
    Inner triplets (present & High Luminosity Upgrade)
    Simulation and experimental studies for the LHC injector complex (PS and SPS)
      Pre-shutdown machine qualification w.r.t. e-cloud
      LHC injectors upgrade scenarios
      Scrubbing and mitigation strategies
Not covered in this presentation

## Slide 67
Thanks for your attention!
Thanks to:
G. Arduini, H. Bartosik, D. Banfi, V. Baglin, C. Bhat, R. De Maria, O. Dominguez,
M. Driss Mensi, E. Metral, J. Esteban-Muller, W. Hofle, K. Li, H. Maury Cuna, H. Neupert, T. Pieloni,
G. Papotti, F. Roncarolo, E. Shaposhnikova, M. Taborelli, L. Tavian, G. Trad, C. Y. Vallgren,
D. Valuch, C. Zannini, F. Zimmermann
ABP, Collimation, Cryogenics, EN/STI, Injection, Operation, Transverse Damper, Vacuum teams

## Slide 69: Proposed strategy for LHC start up in 2015: Summary
Commissioning (low intensity / luminosity)
Vacuum conditioning (50ns/short trains 25ns)
(5-7 days)
50ns
(intensity ramp up + physics)
Scrubbing with 25ns
(2 days)
δdip≥2.2
δdip≈2.2
δdip≤2.
450GeV
6.5 – 7 TeV
Intensity ramp up & physics with 25ns
25ns scrubbing
(5 days)
25ns test ramps + commissioning (≈ 5 days)
Scrubbing with doublet beams
(≈ 5 days)
450GeV
6.5 – 7 TeV
δdip≤2.
δdip≈1.45
δdip≤1.4